# Electrical, Computer, and Systems Engineering

# ECSE-4670:  CCN

# Fall 1999

# Problem Set 1- Due Tuesday, September 17th 1999

| Your Name |  |
| --- | --- |

# Notes:

- Be brief.

- A part of the homework credit is given to reading. Reading assignments will be quizzed in both informal and formal quizzes

- Please write your answers on separate sheets and staple it along with the questions to facilitate easy grading.

--------------------------------Do not write below this line-----------------------------------------

| 1 | 2 | 3 | 4 | Total |
| --- | --- | --- | --- | --- |
| 20 | 10 | 10 | 10 | 50 |

# TA Signature :___________________________________

- Reading assignment:

- Read the textbook (Tanenbaum) Chap 1. Summarize key concepts and issues NOT covered in class.

- Concepts: (Multiplexing) What is multiplexing and how does it improve system design ? Why is statistical multiplexing not good for systems whose load characteristics have no variation ? Why is packet switching more efficient than circuit switching ?

- Concepts: (Virtualization) A switch, using a switching table, moves packets from one port to another. What is the virtualization provided by a switch ? Where are the “multiplexing” and “indirection” components required to provide this virtualization? Similarly describe the virtualization obtained when a labeled set of sources

- Problem: (Metrics/Parameters)  Metric m1 can be expressed as the following functions of parameters p1, p2 and p3:

M1 = (0.002*p1  + 2*p2 + p3)

Where p1 has the range [0,1], p2 has the range [10,100] and p3 has the range [1000, 10,000]. Which is the most dominant parameter amongst p1, p2 and p3, if I define “dominant” as

- that parameter which affects M1 by a unit change in its value?

- that parameter which affects M1 by varying by the maximum amount in its range ?

Suppose M1 is “response time” and I discover a design breakthrough which changes  the

coefficient  of p2 to 1 (from 2).  What is the maximum and minimum speedup I can attain,

assuming p1=0 and p3=1000 ? (speedup = new M1/old M1)