# Electrical, Computer, and Systems Engineering

# ECSE-4670:  CCN

# Fall 1999

# Problem Set 2- Due Monday, October 4th 1999

| Your Name |  |
| --- | --- |

# Notes:

- Be brief and precise, but complete in your answers

- A part of the homework credit is given to reading. Reading assignments will be quizzed in both informal and formal quizzes

- Please write your answers on separate sheets and staple it along with the questions to facilitate easy grading.

--------------------------------Do not write below this line-----------------------------------------

| 1 | 2 | 3 | 4 | 5 | Total |
| --- | --- | --- | --- | --- | --- |
| 20 | 5 | 5 | 10 | 10 | 50 |

# TA Signature :___________________________________

- Reading assignment:

- Read the textbook (Tanenbaum) Chap 2 and 3. Summarize key concepts and issues NOT covered in class. For each concept/issue a one-line descriptive summary is what is required, nothing more or less.

- Concepts: (Modulation/Coding) What is/are the functional difference(s) between modulation techniques like ASK, PSK, FSK and signaling/coding schemes like NRZ/Manchester etc ?  Given a data rate of 10 Mbps (like Ethernet) and the use of Manchester  encoding, what is the resultant baud rate?

- Problem: (Nyquist/Shannon limits) A cable operator wants to convert a regular 6 MHz TV channel to carry data using 4-level signals. What is the maximum data rate he can expect from the channel ? Even if he had the luxury of choosing an arbitrary numbers of levels in signaling, given that the S/N ratio is 20 dB, what is the maximum data rate possible ?

- Problem (Error Detection): What is the Hamming distance of the codespace containing the following three code words: 010101, 001111 and 001010 ? What is the maximum Hamming distance possible using  6-bit codewords (assuming at least two codewords) ? Given the CRC polynomial P(x)= x5 + x4 + x2 + 1 and the message payload, M = 1110001101,  find the bit pattern T calculated from the CRC procedure which will be transmitted on the wire.

- Problem (Flow Control/Error Recovery): Complete the missing steps in the derivation of the performance of the Go-back-N ARQ procedures based upon slides 41-44 in the handout. Your goal is to derive an expression for the channel utilization U in terms of the window size, N, loss probability P and the ratio of propagation-to-transmission times, (.