68HC12 Timer & Counter Operation Modes (read text for details)

1. A single Free Running Counter – TCNT ($0084:$0085)

16 bits, counts M-clock cycles (divided by PRESCL value)

[Random # Generator]

2. Timer Overflow Interrupts

Interrupt vector $FFDE:$FFDF (#15)

3. Timer Output Compare

8 channels available: TC0 – TC7

When 16 bit Free Running Counter matches 16 bits in Output Compare Register, a Flag, TFLGn, is set

Can be configured to set bits on Port T

[Works as an alarm clock]

4. Timer Input Capture

8 channels available: TC0 – TC7 (same as in 3 – shared resources)

Port T bits 0 – 7 are used to signal hardware to store Free Running Counter value into specified register and set a Flag, TFLGn

[May be used to measure period of a signal, save the occurrence time of events]

5. Pulse Accumulator – 2 sub-modes

Input pulses on Port T bit 7 counted in PACNT (16-bit counter)

Event counter

Count pulses in PT7

Gated timer accumulator

Count (M-clock pulses)/64 gated by PT7 (only count when PT7 is on)

Overflow Interrupt vector $FFDC:$FFDD (#14)

Pulse input edge Interrupt vector $FFDA:$FFDB (#13)

6. Real-Time Interrupt

Similar to Timer Overflow Interrupt except that the rate is programmable

RTI Interrupt vector $FFF0:$FFF1 (#24)

[Adjustable interval timer – select one of 8 values with RTR2:RTR0]

7. Pulse Accumulator & Free Running TCNT counter combined for 24- or 32-bit counters

68HC912B (not MPSD EVB) Pulse Width Modulator

[Continuously variable control of DC Motors, Heaters, Lights, etc.]