Memory Decoding

(8-bit data bus example)

NOTE: Glue logic is not optional! Leaving out the proper chip selection logic when adding memory to the EVB will crash the processor.

000016

8k x 8 bits

1FFF16

200016

8k x 8 bits

3FFF16

Incomplete Address Decoding

Can also ignore A15 & A14, but then physical memory values will appear at multiple addresses! Note: 16k requires 14 address bits.

A15

A14

A13	Used with CSDn for chip select signal

A12

A0

Now the 16k block (8k + 8k) will appear 4 times in the 64k range,

000016 – 3FFF16 = 400016 – 7FFF16 = 800016 – BFFF16 = C00016 – FFFF16

since A15 and A14 are ignored and match any value!

8-bit Data Bus Configuration Question

What is the address range of this 4k-memory block?

____ XXXX XXXX XXXX

or

____ 0000 0000 0000  ->  ____ 1111 1111 1111

# Text boxes

8 bit data bus, 13 address lines/8k block

0 – 1FFF

000X XXXX XXXX XXXX

o

Top 3 address lines & CSDn used to create chip select signal

o

Connected to chip address lines

Not used

R/W

CS

A15

A14

A13

A12

HC12

A11

…

A0

D7

…

D0

WE

OE

CE

RAM

A11

…

A0

D7

…

D0

Memory Mapping a D-FF to a single bit (Address = 200016, bit D0)