Memory Decoding

(8-bit data bus example)

NOTE: Glue logic is not optional! Leaving out the proper chip selection logic when adding memory to the EVB will crash the processor.

000016

8k x 8 bits

1FFF16

200016

8k x 8 bits

3FFF16

Incomplete Address Decoding

Can also ignore A15 & A14, but then physical memory values will appear at multiple addresses! Note: 16k requires 14 address bits.

A15

A14

A13	Used with CSDn for chip select signal

A12

A0

Now the 16k block (8k + 8k) will appear 4 times in the 64k range,

000016 – 3FFF16 = 400016 – 7FFF16 = 800016 – BFFF16 = C00016 – FFFF16

since A15 and A14 are ignored and match any value!

8-bit Data Bus Configuration Question

What is the address range of this 4k-memory block?

____ XXXX XXXX XXXX

or

____ 0000 0000 0000  ->  ____ 1111 1111 1111

| $0000 | 00k | } 2k } 2k } 2k } 2k } 2k } 2k } 2k } 2k | } 4k } 4k } 4k } 4k | }8k }8k |
| --- | --- | --- | --- | --- |
| $0800 | 02k |  |  |  |
| $1000 | 04k |  |  |  |
| $1800 | 06k |  |  |  |
| $2000 | 08k |  |  |  |
| $2800 | 10k |  |  |  |
| $3000 | 12k |  |  |  |
| $3800 | 14k |  |  |  |
| $4000 | 16k |  |  |  |

2k Memory Blocks (8-bit):

XXXX 1000 0000 0000 = 211 = 2k : 11 address bits (XXXX X000 0000 0000 – XXXX X111 1111 1111)

[ A15  A14  A13  A12  A11 ] A10  A9  A8  A7  A6  A5  A4  A3  A2  A1  A0

. . . | $1000 - $17FF | $1800 - $1FFF | $2000 - $27FF | $2800 - $2FFF | $3000 - $37FF | $3800 - $3FFF |

4k Memory Blocks (16-bit as 2 x 2k x 8-bit, 2 x 2kbyte = 4kbyte):

XXX1 0000 0000 0000 = 212 = 4k : 11+1 address bits		Boundaries for ( 2k x 8-bit ) x 2 memories

[ A15  A14  A13  A12 ] A11  A10  A9  A8  A7  A6  A5  A4  A3  A2  A1 [ A0 ]

[   0       0       1       0   ]

[   0       0       1       1   ]

. . . | $1000 - $1FFF | $2000 - $2FFF | $3000 - $3FFF |

8k Memory Blocks (16-bit as 16 x 4k x 1-bit, 16 x 4kbit = 8kbyte):

XX10 0000 0000 0000 = 213 = 8k : 12+1 address bits		Boundaries for ( 4k x 1-bit ) x 16 memories

[ A15  A14  A13 ] A12  A11  A10  A9  A8  A7  A6  A5  A4  A3  A2  A1 [ A0 ]

[   0       0       1   ]

. . .  . . .  | $2000 - $3FFF |

Memory glue logic Truth-Table

Logic for Chip Selection pin on Memory DIP

| R* | W* | A0-A10 | A11 | A12 | A13 | A14 | A15 | R/W*, WE*, W* | E*, CE*, CS* | OE* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2k x 8-bit + 2k x 8-bit ( 4kBytes (0x2000 – 0x2FFF)	2 DIPs

{4k x 1-bit} x 16 ( 8kByte (0x2000 – 0x3FFF)		16 DIPs, but only wire up 4: 2 starting at 0x2000 and 2 starting at 0x3000

# Text boxes

8 bit data bus, 13 address lines/8k block

0 – 1FFF

000X XXXX XXXX XXXX

Top 3 address lines & CSDn used to create chip select signal

o

o

Not used

Connected to chip address lines

WE

OE

CE

RAM

A11

…

A0

D7

…

D0

R/W

CS

A15

A14

A13

A12

HC12

A11

…

A0

D7

…

D0

Memory Mapping a D-FF to a single bit (Address = 200016, bit D0)