C8051F120 SYSCLK Clock Frequencies

See Reference Manual, Ch 14, Fig 14.1

| SOURCES | 3 main sources on C8051F120 | Final SYSCLK ( 100MHz |  |  |
| --- | --- | --- | --- | --- |
| Internal | 24.5MHz (factory calibrated) | OSCICN.1-0 (IFCN1-IFCN0) | Good accuracy ((2%) |  |
|  | ( 1 = 24.5MHz | 11 |  |  |
|  | ( 2 = 12.25MHz | 10 |  |  |
|  | ( 4 = 6.125MHz | 01 |  |  |
|  | ( 8 = 3.0625MHz (default) | 00 |  |  |
|  | Enable | OSCICN.7 (IOSCEN) |  |  |
| External |  | OSCXCN.6-4 (XOSCMD2-XOSCMD0) |  |  |
|  | XTAL ( 2 = 11.0592MHz | 111 | Highest accuracy (50ppm, ±0.005%) |  |
|  | XTAL = 22.1184MHz | 110 |  |  |
|  | RC / C ( 2 | 10X |  |  |
|  | CMOS ( 2 | 011 |  |  |
|  | CMOS | 010 |  |  |
|  | Off (disabled) | 00X |  |  |
| PLL Modified Int. or Ext. Source | See Reference Manual Fig 14.2 | Provide a wide range of frequencies | Highest accuracy when XTAL used |  |
|  |  | PLL0DIV.4-0 (PLLM4-PLLM0) |  |  |
|  | 25MHz ( Freq ( 100MHz | PLLM is a 5-bit binary # |  |  |
|  | 5MHz ( SourceFreq ( 30MHz | PLL0MUL.7-0 (PLLN7-PLLN0) |  |  |
|  |  | PLLN is an 8-bit binary # |  |  |
| Source Ready Flags | Internal Oscillator ready | OSCICN.6 (IFRDY) |  |  |
|  | Crystal Oscillator valid | OSCXCN.7 (XTLVLD) |  |  |
|  | PLL Oscillator locked | PLL0CN.4 (PLLLCK) |  |  |

NOTE: 22,118,400 = 52x33x215 = 25x27x32,768 = 675x32,768

Start sequence for crystal oscillator:

Start up processor (default frequency = 24.5MHz/8 = 3.0626MHz

Enter “lock-in” range for crystal frequency [OSCXCN.2-0 (XFCN2-XFCN1)]

Turn on crystal oscillator & wait until stable & valid [OSCXCN.7 (XTLVLD)]

Select new SYSCLK source [CLKSEL.1-0 (CLKSL1-CLKSL0) = 01]

Start sequence for PLL oscillator:

Start source oscillator if not running

Power up and enable PLL [PLL0CN.0 (PLLPWR), PLL0CN.1 (PLLEN)]

Select source input (internal or external) [PLL0CN.2 (PLLSRC)]

Set multiply and divide values [PLL0MUL, PLL0DIV]

Enter proper “lock-in” range values based on PLL output frequency

[PLL0FLT.5-4 (PLLICO1-PLLICO0), PLL0FLT.3-0 (PLLLP3-PLLLP0)]

Wait until stable & locked [PLL0CN.4 (PLLLCK)]

Select new SYSCLK source [CLKSEL.1-0 (CLKSL1-CLKSL0) = 10]

SYSCLK may be directed to be an output on the Crossbar (/SYSCLK) and may have an additional divide by of 1, 2, 4, or 8 to be used to clock external logic circuits [CLKSEL.5-4 (CLKDIV1-CLKDIV0)]

The Crossbar must be configured to have the output made available.