C8051F120 VREF Reference Voltage

SFR PAGE 0 = ADC0_PAGE

Voltage references are needed before the ADCs or DACs may be used.

See Reference Manual, Ch 9, Fig 9.1

| SOURCES | 5 main sources on C8051F120 |  |  |  |
| --- | --- | --- | --- | --- |
| Internal | NOTE: BIASE must be set to 1 for all ADC & DAC, even if external source is used. |  |  |  |
|  | 2.4V = 1.2V(Band-gap) x 2 | REF0CN.1-REF0CN.0 (BIASE & REFBE) | High accuracy (15ppm/°C) |  |
|  | DAC0 output (to ADC0) | REF0CN.4 (AD0VRS) |  |  |
|  | 3.3V (AV+) pwr supply (to ADC2) | REF0CN.3 (AD2VRS) |  |  |
| External | Make sure REFBE = 0 (bias buffer is OFF) before applying voltage to REF0. |  |  |  |
|  | Any stable voltage supply ( 3.3V (AV+ - 0.3V) | REF0: J20, pin 7 AGND: J20, pin 8 | Accuracy of chosen supply |  |
| Stabilize VREF with C | 4.7(F tantalum & 0.1(F ceramic capacitors | Connect C between AGND & VREF | See Reference Manual Fig 9.1 |  |
| Distribution of VREF |  |  |  |  |
|  | To ADC0 & ADC2 | REF0CN.4-REF0CN.3 (AD0VRS-AD2VRS) |  |  |
|  | To DAC0 & DAC1 | Fixed to VREFD |  |  |
|  | VREF ( VREFD | J22, 1-2 | Jumper Block: |  |
|  | VREF ( VREF0 | J22, 3-4 | See Development |  |
|  | VREF ( VREF1 | J22, 5-6 | Kit Users Guide |  |
|  |  |  | Section 7.9 |  |
| Temperature Sensor | Power up sensor, enable output to ADC0 AMUX channel 9 | REF0CN.2 (TEMPE) |  |  |

NOTE: With ADC0 in differential mode, negative voltages down to –VREF may be input and converted into 2’s compliment binary numbers. This is done without supplying a voltage value of –VREF to the processor.

VDD is the digital power supply voltage (+2.7V - +3.6V range, but 3.3V is used on EVB),

DGND is the corresponding digital supply ground

AV+ is the analog power supply voltage (+2.7V - +3.6V range, but 3.3V is used on EVB),

AGND is the corresponding analog supply ground