SRPT.DOC

						Lance Lascari WS2B 4/93


		This document is an attempt at shedding some light on the 
	innards of the "WS2B Small Repeater Controller.  I won't attempt
	to explain all of the code, but mainly certain sections that I feel
	demand it.

TIMING:
	All timing in the controller is derived from the timer overflow 
	interrupt.  I liked this idea since it takes almost no effort to
	implement.  Every 33 mS  ( when running the hc11 on an 8 mHz clock )
	the interrupt fires and updates all of the "system" counters.  The 
	main loop of the program just periodically compares the values of the
	counters to a threshold value and performs the appropriate actions.

TONE GENERATION:
	Tones necessary for the CW ID are produced using the output
	compare timer system.  The output compare counters are just loaded 
	with the tone's half_cycle delay value each time the interrupt fires
	and this toggles the output bit on/off at a rate equal to the tone.
	Yes, this does produce a square wave, so it is desirable to use a
	low-pass filter of sorts on the output to reduce the harmonic content.
	The tone is keyed on and off by enabling and disabling the interrupt.
	This same technique with changes only in the filter would  allow for 
	nice CTCSS tone generation.

MORSE GENERATION:
	The Morse code routines in the controller are by far my favorite.
	This work was derived from some similar routines for the 68705 
	written by Dave Page KD3NC and myself about 3 years ago.  The changes
	are quite extensive. The reason for the changes were as follows;

	A) I wanted something that was mostly my work
	B) Why not try it a different way
	C) Get away from S-COMM ( popular repeater controller ) type CW codes.
           ( If you wish to look at the cw routines that use the "S-COMM" 
	     technique, see the hc11 beacon code )
     	D) wanted a quick and easy way (not the best, but simple) to reduce
	   the size of the cw data table.

			   "How it works."
	This part is pretty straight forward.  The routine SEND_CW takes a 
	pointer (CW_DATA) to the string of cw chars. to be sent, and sends
	them one by one ( the string terminator is $FF ).  As the chars are
	read one by one, SEND_CW passes them to the SENDCW_CHR routine
	where they are indexed in a table, formed with the proper delays and
	sent.
       
		More detail you say ?
	
	  	When the char is read from the string and sent to SENDCW_CHR,
	it resides in accb.  Index register Y is  then loaded with the 
	beginning of the cw table.  The structure of the table is as follows
	  (sample entry  for the letter "A") 
============================================================================
          FCB      'A',1,2,0             ;A-1
============================================================================
		 ^^ ascii A, 1=dit, 2=dah, 0=end of entry
       
	Now, what SENDCW_CHR does is scans the table, looking for a match with
	the contents of ACCB ( The ascii representation of the char ).  At 
	this point, it takes the 1's ,2's, 3's and 0's, and makes them into
	dits, dahs, pauses, and "ends" respectively.

		The older routines ( those found in the beacon code ) are 
	faster because they can immediately calculate where each entry in
	the table is, but they have their drawbacks.  The main drawback being
	that each table entry REQUIRES 8 bytes of stuff for spacing no matter
	what.  I think with these routines  I saved a hundred bytes or so.
	(that was certainly something to consiter when I was trying to fit
	all of the code for the controller in the 2k EEPROM. )  With a little
	more optimization, at least 30 - 40 bytes more could be spared.

DTMF:
		Since I'm not a bandwidth hungry DSP jock, I used a touch-tone
	decoder IC (SSI 75T202) to detect DTMF tones.  The chip is tagged onto
	an input port, and the "DATA VALID" line is tied to the IRQ pin on the
	HC11.  Thus when a valid tone is detected, an interrupt fires and the
	HC11 grabs the 4bit value of the tone from the I/O port.  

		From a user standpoint, the DTMF strings are of fixed length
	N, with a '*' char as the terminator, and the '#' char is used 
	to clear the buffers in case you screw up.

		The interrupt service routine grabs a string of DTMF digits
	of length NUM_O_DIGS ( * in the interrupt service routine I had
	to use the number directly in some cases instead of the equate because
	my assembler couldn't handle  the necessary number of chars in the 
	parameter :(  ).  As far as operation is concerned, the string is
	a fixed length.  If a string is received longer than N chars or the
	star digit is received before N chars are received, an ERR message is 
	sent.  The interrupt service routine WILL NOT accept any new  input 
	until the last batch of input is completely processed.  This is 
	accomplished by the strategic setting / clearing of the DTMF_FLAG. 
         
    ** Here's where the heavy mountain dew consumption begins: **

		( much of this code isn't very elegant, but it seems to work
		  OK.  It should be pretty obvious that I'm not a CS person :)

		Once all of the digits are loaded by the interrupt service 
	routine, the DTMF_FLAG is set, signalling DTMF_CHK that it has some
	work to do.  DTMF_CHK basically goes through the string, comparing it
	to all of the others stored in the COMMAND STRING TABLE  (starting 
	addr C_1_ ).  For each of the command strings in memory, it increments
	an individual counter for each matched digit.  Then, once this is 
	is complete, the counter values that equal the number of digits in
	the control strings are consitered a "match" ( i.e. if command strings
	are of length 4, and a given counter equals 4, then a valid match has
	occurred ).
       
		Now that DTMF_CHK has done it's work, CMD_EXE scans through
	the counters corresponding to the various commands looking for the
	discussed "match" condition.  For each command there is an entry in
	the SUB_TABLE.  SUB_TABLE consists of a set of jump instructions and
	addresses corresponding to the actual code/subroutines that each
	command will execute.  Anyway, CMD_EXE scans the counters in order, 
	and at the same time, keeps index register Y pointing at the 
	appropriate jump table entry (SUB_TABLE).  Thus, when the "match" 
	counter is found , the appropriate commands can be executed by doing
	a " JMP 0,Y " .  Note that because I used JMP's here, the command 
	subroutines will return to CMD_EXE if/when they perform the RTS 
	instruction.

		That's about it for the dtmf routines.  There are certainly
	some redundancies, but I haven't noticed any real problem with 
	performance.  I wrote them this way because I wanted to be able to
	have any number of commands that I wanted by just changing some 
	assembler directives (even though I haven't fully implemented this 
	yet).  In a sense, I felt this was the most flexible structure for 
	handling a number of DTMF commands.  I'm not sure I met the 
	"elegant code" criteria in my own mind... but oh well.


		      ****** DISCLAIMERS ******
	
		This repeater controller has been in service for a few months
	now, doing a pretty decent job ( W2SZ/R 443.000 + , Troy , NY ).  
	I haven't worked out all of the bugs because I've been busy , my 
	handheld doesn't generate tones that the 75t202 is fully satisfied 
	with, and my handheld's battery is on  it's last legs.  SRPT.ASM was 
	written over a long weekend, with some bug fixes and optimizations 
	over time.  It was not intended as a full featured, programmable, 
	coffee-maker repeater controller.  Instead, it was just one of those
	things I wanted to do.

	       
			******* Future ******
		I think there are a few hundred bytes of eeprom left .....

	 I've thought of implementing the following features into SRPT:
		
		1) DTMF command driven readout of A/D port
		   ( almost like telemetry )
	
		2) CTCSS encode/decode ( not a whole lot of drive to do this )
		
		3) autopatch ( mostly a hardware effort )
		
		/* insert your own $0.02 here */